Network Working Group                    S. Brorson (Axiowave Networks)

Internet Draft                     S. Dharanikota (Nayna Networks, Inc)

Expiration Date: January 2001               J. Drake (Calient Networks)

W. L. Edwards (iLambda Networks)

R. Goyal (Axiowave Networks)

R. Krishnan (Axiowave Networks)

J. Shantigram (PhotonEx Corp.)

E. Snyder (PhotonEx Corp.)

George Swallow (Cisco Systems)

G. Tumuluri (Calient Networks)

Y. Xue (UUNET/WorldCom)

J. Yu (Zaffire, Inc)

Editors:

Andre Fredette (PhotonEx Corp.)

Jonathan Lang (Calient Networks)

July 2001

Link Management Protocol (LMP) for WDM Transmission Systems

draft-fredette-lmp-wdm-02.txt

Status of this Memo

This document is an Internet-Draft and is in full conformance with

all provisions of Section 10 of RFC2026 [RFC2026].

Internet-Drafts are working documents of the Internet Engineering

Task Force (IETF), its areas, and its working groups. Note that

other groups may also distribute working documents as Internet-

Drafts.

Internet-Drafts are draft documents valid for a maximum of six

months and may be updated, replaced, or obsoleted by other documents

at any time. It is inappropriate to use Internet- Drafts as

reference material or to cite them other than as "work in progress."

The list of current Internet-Drafts can be accessed at

http://www.ietf.org/ietf/1id-abstracts.txt

The list of Internet-Draft Shadow Directories can be accessed at

http://www.ietf.org/shadow.html.

[Page 1]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

ABSTRACT

A suite of protocols is being developed in the IETF to allow

networks consisting of photonic switches (PXCs), optical

crossconnects (OXCs), routers, switches, DWDM transmission systems,

and optical add-drop multiplexors (OADMs) to use an MPLS-based

control plane to dynamically provision resources and to provide

network survivability using protection and restoration techniques.

As part of this protocol suite, the Link Management Protocol (LMP)

[LMP] is defined to "maintain control channel connectivity, verify

component link connectivity, and isolate link, fiber, or channel

failures within the network."  In it's present form, [LMP] focuses

on peer communications (eg. OXC-to-OXC).  In this document we

propose extensions to LMP for use with DWDM transmission systems.

These extensions are intended to satisfy the "Optical Link Interface

Requirements" described in [OLI].

CONTENTS

1. Introduction.......................................................3

2. LMP Extensions for WDM Transport Systems...........................5

2.1. Control Channel Management.......................................5

2.2. Link Verification................................................6

2.3. Link Summarization...............................................6

2.3.1. Link Group ID..................................................7

2.3.2. Link Descriptor................................................8

2.3.3. Shared Risk Link Group Identifier (SRLG):.....................10

2.3.4. Wavelength....................................................10

2.3.5. Bit Error Rate (BER) Estimate.................................11

2.3.6. Optical Protection............................................11

2.3.7. Span Length:..................................................13

2.3.8. Administrative Group (Color)..................................13

2.4. Fault Management................................................13

2.4.1. ChannelStatus Message (MsgType = TBD).........................14

2.4.1.1. Channel Status TLV..........................................15

2.4.1.2. Group Status TLV............................................16

2.4.2. ChannelStatusAck Message (MsgType = TBD)......................17

2.4.3. ChannelStatusReq Message (MsgType = TBD)......................18

2.4.3.1. Channel Entity TLV..........................................18

2.4.3.2. Group Entity TLV............................................19

2.5. Trace Monitoring................................................19

2.5.1. TraceMonitor Message (MsgType = TBD)..........................19

2.5.1.1. SONET Section Trace TLV.....................................20

2.5.1.2. Trace TLV...................................................21

2.5.2. TraceMonitorAck Message (MsgType = TBD).......................22

2.5.3. TraceMonitorNack Message (MsgType = TBD)......................22

2.5.4. TraceMismatch Message (MsgType = TBD).........................23

2.5.5. TraceMismatchAck Message (MsgType = TBD)......................24

2.5.6. TraceReq Message (MsgType = TBD)..............................25

2.5.7. TraceReport Message (MsgType = TBD)...........................25

3. Security Considerations...........................................26

4. References........................................................27

5. Author's Addresses................................................28

[Page 2]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

1. Introduction

Future networks will consist of photonic switches (PXCs), optical

crossconnects (OXCs), routers, switches, DWDM transmission systems,

and optical add-drop multiplexors (OADMs) that use the GMPLS control

plane to dynamically provision resources and to provide network

survivability using protection and restoration techniques.  A pair

of nodes (e.g., a PXC and a DWDM system) may be connected by

thousands of fibers. Furthermore, multiple fibers and/or multiple

wavelengths may be combined into a single bundled link.  [LMP]

Defines the Link Management Protocol (LMP) to "maintain control

channel connectivity, verify component link connectivity, and

isolate link, fiber, or channel failures within the network."  In

it's present form, [LMP] focuses on peer communications (eg.  OXC-

to-OXC) as illustrated in Figure 1.  In this document, extensions to

LMP for use with DWDM transmission systems are proposed.  These

extensions are intended to satisfy the "Optical Link Interface

Requirements" described in [OLI].  It is assumed that the reader is

familiar with LMP as defined in [LMP].

+------+       +------+       +------+       +------+

|      | ----- |      |       |      | ----- |      |

| OXC1 | ----- | WDM1 | ===== | WDM2 | ----- | OXC2 |

|      | ----- |      |       |      | ----- |      |

+------+       +------+       +------+       +------+

^                                               ^

|                                               |

+----------------------LMP----------------------+

Figure 1: Current LMP Model

A great deal of information about a link between two OXCs is known

by the DWDM transmission system.  Exposing this information to the

control plane via LMP can improve network usability by further

reducing required manual configuration and also greatly enhancing

fault detection and recovery.  Fault detection is particularly an

issue when the network is using all-optical photonic switches (PXC).

Once a connection is established, PXCs have only limited visibility

into the health of the connection.  Even though the PXC is all-

optical, long-haul DWDM transmission systems typically terminate

channels electrically and regenerate them optically, which presents

an opportunity to monitor the health of a channel between PXCs.  The

model for extending LMP to WDM transmission systems is shown in

Figure 2.

[Page 3]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

+------+       +------+       +------+       +------+

|      | ----- |      |       |      | ----- |      |

| OXC1 | ----- | WDM1 | ===== | WDM2 | ----- | OXC2 |

|      | ----- |      |       |      | ----- |      |

+------+       +------+       +------+       +------+

^  ^             ^              ^            ^  ^

|  |             |              |            |  |

|  +-----LMP-----+              +-----LMP----+  |

|                                               |

+----------------------LMP----------------------+

Figure 2: Extended LMP Model

In this model, an OXC may have multiple LMP sessions corresponding

to multiple peering relationships.  At each level, LMP provides link

management functionality (i.e., control channel management, physical

connectivity verification, link property correlation) for that

peering relationship.  For example, the OXC-OXC LMP sessions in

Figure 2 are used to build traffic-engineering (TE) links for GMPLS

signaling and routing, and are managed as described in [LMP]. At the

transport level, the OXC-WDM LMP session (shown in Figure 2) is used

to augment knowledge about the links between the OXCs.  The

management of these LMP sessions is discussed in this draft. It is

important to note the an OXC may peer with one or more OLS’s and an

OLS may peer with one or more OXC’s.

Although there are many similarities between an OXC-OXC LMP session

and an OXC-WDM LMP session, particularly for control management and

link verification, there are some significant differences as well.

These differences can primarily be attributed to the nature of an

OXC-WDM link, and the purpose of OXC-WDM LMP sessions.  As

previously mentioned, the OXC-OXC links provide the basis for GMPLS

signaling and routing at the optical layer.  The information

exchanged over LMP-WDM sessions is used to augment knowledge about

the links between OXCs.

There is a lot of focus on "getting additional knowledge" of links, but little on interaction between WDM and OXC for provisioning & management purposes (e.g., suppressing alarms/trace monitoring/etc). In fact, I believe these latter functions are more important applications for OLI than getting link information. You might want to give a better perspective of the provisioning and management problem here and explain how LMP-WDM helps.

In order for the information exchanged over the OXC-WDM LMP sessions

to be used by the OXC-OXC session, the information must be

coordinated by the OXC.  However, the two LMP sessions are run

independently and MUST be maintained separately.  One critical

requirement when running an OXC-WDM LMP session is the ability of

the WDM to make a data-bearing link transparent when not doing the

verification procedure.  This is because the same data-bearing link

may be verified between OXC-WDM and between OXC-OXC.  Currently, the

BeginVerify procedure is used to coordinate the Test procedure (and

hence the transparency/opaqueness of the data-bearing links) as

described in [LMP].

This assumes that the same overhead bytes may be used for LMP and LMP-WDM. Why should this be the case? In fact, it should be considered whether separate set of OH bytes be mandated for these purposes.

[Page 4]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

To maintain independence between the sessions, it MUST be possible

for the LMP sessions to come up in any order.  In particular, it

MUST be possible for an OXC-OXC LMP session to come up without an

OXC-WDM LMP session being brought up, and vice-versa.

I would state this even stronger. There should be no assumptions on whether even (regular) LMP is running between OXCs. Isn't it the case that even GMPLS is not mandated to use OLI? I would completely decouple LMP from LMP-WDM (other than of course for reusing LMP design and message paradigms in LMP-WDM).

This draft focuses on extensions required for use with opaque

transmission systems.  Work is ongoing in the area of completely

transparent wavelength routing; however, it is premature to identify

the necessary characteristics to advertise.  That said, the protocol

described in this document provides the necessary framework in which

to advertise additional information as it is deemed appropriate.

Additional details about the extensions required for LMP are

outlined in the next section.

2. LMP Extensions for WDM Transport Systems

As currently defined, LMP consists of four types of functions:

1. Control Channel Management

2. Link Verification

3. Link Summarization

4. Fault Localization

It is very important to understand the subtle distinctions between

the different types of links being considered in the extended LMP-

WDM.  For example, in Figure 2 when OXC1 and OXC2 complete the

verify process, the links being verified are the end-to-end links

between the OXC's.  It is the TE link composed of these "ports" or

"component links" that are advertised in the routing protocols and

used for the purposes of connection setup.  The verify procedure

between OXC1 and WDM1, on the other hand verifies the shorter link

between these two nodes.  However, each of these shorter links is a

segment of one of the larger end-to-end links.  The verify serves

two functions: to verify connectivity and exchange handles by which

each port or component link is referred.  Furthermore, it is up to

the OXC to correlate the handles between the various LMP sessions.

Once a control channel has been established and the OXC-WDM

verification procedure has been completed successfully, the OXC and

WDM transmission system may exchange information regarding link

configuration (link summarization).  An OXC may also receive

notification from a WDM transmission system (fault notification).

In subsequent sections, specific changes are proposed to extend LMP

to work with WDM transmission systems.

2.1. Control Channel Management

[Page 5]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

As in [LMP], we do not specify the exact implementation of the

control channel; it could be, for example, a separate wavelength or

fiber, an Ethernet link, an IP tunnel through a separate management

network, or the overhead bytes of a data-bearing link.

For any of the in-band mechanisms (wavelength, OH bytes, etc), more specification is needed. I.e., it has to be specified which wavelength or OH bytes should be used. If this is not specified in this document, refer to a place where it is (or will be) specified. (Otherwise, there is no interoperability.) Also, I'm not even sure if OH bytes in a "data bearing link" can be used, since the OXC could be transparent (the main candidate case for OLI).

The control channel management for OXC-WDM links is the same as for

OXC-OXC links, as described in [LMP].  The LMP Capability TLV

includes a flag indicating support of an OXC-WDM LMP session as

described in this  draft.  Furthermore, a flag has been added to the

LMP Common Header to identify the transmitting node as a DWDM

system.

This description needs to be expanded. Specifically,

- what does the LMP-WDM common header look like? In particular, what's the semantics of the "Local CCID/TE Link ID" field? For LMP-WDM, the concept of a "TE link" seems unncessary. Perhaps this could be called "physical link". Such details are missing here.

- What is the requirement on Node Ids? Should they be unique across a system of OXCs and WDM? Or, should they be only unique between pairs of communicating OXC and WDMs? (Note that OXCs and WDMs may be administered by different entities. How to you ensure system-wide unique Node Ids?)

- What are the negotiable and non-negotiable TLVs in the config message?

- Why can't we always let the OXCs choose all values (e.g., Hello parameters) and the WDM systems to just accept these? I.e., the config procedure could be specified such that only an OXC may initiate it (rather than WDM). Other than the notification process, the OXC mostly controls all transactions, so why can't it dictate the parameters also?

2.2. Link Verification

The Test procedure used with WDM transmission systems is the same as

described in [LMP].  The VerifyTransportMechanism (included in the

BeginVerify and BeginVerifyAck messages) is used to allow nodes to

negotiate a link verification method and is essential for

transmission systems which have access to overhead bytes rather than

the payload.  The VerifyId (provided by the remote node in the

BeginVerifyAck message, and used in all subsequent Test messages) is

used to differentiate Test messages from different LMP sessions.

Link verification under LMP needs some clean up. Specifically,

- The way it is specified currently, you have to configure which links go to which neighbor and which control channel is associated with which sets of links. If you do this much, you might as well configure the port Ids. If you don't do this, the protocol complexity increases.

- The hardware support needed for this has to be clearly stated, as in the NTIP document.

- Are all the concepts used in LMP necessary here in LMP-WDM? Specifically, the concept of TE links is used in LMP verification which I believe is unnecessary in LMP-WDM. (I have a similar comment for LMP also).

- 4. The choices for sending in-band messages need not be as wide as in LMP. In particular, consider the fact that a Test set has to be used to generate/terminate messages between OXC and WDM. In this case, why not use the payload for sending messages? Or, if there is some advantage with using section OH, use that. Need an analysis of this aspect.Frankly, I'm not sure if it's worth the trouble of doing verification, given the need for the hardware and the minimal functionality the protocol provides.

2.3. Link Summarization

As in [LMP], the LinkSummary message is used to synchronize the

Interface Ids and correlate the properties of the TE link.

Additional type-length values (TLVs) are defined to extend the

LinkSummary message to include link characteristics.  The TLVs

described in the following subsections are transmitted as Data Link

Sub-TLVs in the Data Link TLV (see [LMP]).  The link

characteristics, in general, are those characteristics needed by the

control plane for constraint-based routing and connection

establishment.

The format of the Data Link Sub-TLVs follows the LMP TLV format

given In Section 8.3 of [LMP] and shown below:

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|N|          Type               |            Length             |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                                                               |

//                         (TLV Object)                        //

|                                                               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

.  N: 1 bit

The N flag indicates if the object is a negotiable parameter

(N=1) or a non-negotiable parameter (N=0).

[Page 6]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

Note: none of the Data Link TLVs that are defined in LMP-WDM

are negotiable and the N bit should be set to N=0.

.  Type: 15 bits

The Type field indicates the TLV type.

.  Length: 16 bits

The Length field indicates the length of the TLV object in

bytes.

The following Link Characteristics are advertised on a per component

link (or port) basis.

2.3.1. Link Group ID

A local ID assigned to a group of component links.  This ID can be

used to reduce the control traffic in the case of a failure by

enabling the systems to send a single message for a group instead of

individual messages for each member of the group.  A link may be a

member of multiple groups.  For example, there may be a group

corresponding to a particular wavelength and another group assigned

to a physical fiber.

I don't see the point of this. Isn't it the case that a WDM system always multiplexes all incoming wavelengths onto a single fiber? Then, either a failure affects the whole set of wavelengths (e.g., fiber cut) or a random set of wavelengths. So, it seems like either all the links connecting to the WDM is a group, or each link is a group by itself (i.e., no groups in effect). On what basis can you form any other type of link group?

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|0|         Type = TBD          |          Length = 4           |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                           Group ID                            |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

.  Type: 15 bits = TBD

.  Length: 16 bits = 4

.  Group ID: 32 bits

Group ID 0xFFFFFFFF is reserved and indicates all component

links in a TE link.  All component links are members of Link

Group 0xFFFFFFFF by default.

The Link Group ID feature allows Link Groups to be assigned based

upon the types of fault correlation and aggregation supported by a

given OLS.

For example, a Link Group could be created for each WDM laser.  This

group could then be associated with user ports during

[Page 7]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

discovery/initialization time.  Multiple user ports might even be

associated with a single group (depending on the kind of

multiplexing supported in the system).  If a laser fails, the WDM

system can report a failure on the group.  In the OXC this

translates into the failure of the associated link or links.

Again, I'm lost. Each OXC-WDM physical link, which is what OLI is controlling, has a one-to-one mapping with a laser. How can multiple links be associated with a laser?

Another group could be assigned for a fiber to report all ports down

that are associated with that fiber if LOS is detected at the fiber

level.  Depending on the physical WDM implementation, it may make

sense to allocated other groups, such as all ports on a particular

circuit pack.  With this method, the OXC only needs to know about

the externally visible ports.  The WDM system can associate the

ports with logical groups and the OXC doesn't need to know anything

about the physical WDM implementation or how ports are multiplexed

electrically or optically within the system.

On the whole, this concept seems marginal in value.

2.3.2. Link Descriptor

The Link Descriptor TLV represents the characteristics of the link

comprising the encoding type and bandwidth characteristics.  This

information is needed for constructing a circuit.  The OXC must

match the link information between incoming and outgoing interfaces

for a given path.

Note: This information may be a prerequisite for running the verify

protocol, thus it may be redundant when verify is being used.

Precisely. If verify is not used, then this information should be configured. Furthermore, stuff like link encoding type, reservable bw, etc, have meaning only at the OXC layer (ie., on OXC-to-OXC links). It seems quite unnatural that a WDM system (and its administrators) would even care about this stuff. Also, how does the WDM system even know about link encoding type?

The details for the information in this TLV are the same as those

for the link descriptor sub-TLV defined in [KRB00a].

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|0|         Type = TBD          |          Length = 12          |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                       Link Encoding Type                      |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                  Minimum Reservable Bandwidth                 |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                  Maximum Reservable Bandwidth                 |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

.  Type: 15 bits = TBD

.  Length: 16 bits = 12

[Page 8]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

.  Link Encoding Type: 32 bits

Value        Link Encoding Type

-----        ------------------

1        Standard SONET

2        Arbitrary SONET

3        Standard SDH

4        Arbitrary SDH

5        Clear

6        GigE

7        10GigE

.  Minimum Reservable Bandwidth: 32 bits

Bytes per Second represented in IEEE floating point format.

.  Maximum Reservable Bandwidth: 32 bits

Bytes per Second represented in IEEE floating point format.

If the interface only supports a fixed rate, the minimum and

maximum bandwidth fields are set to the same value.

Bandwidth Values and their IEEE representation for common

interfaces are provided in the following table.

Signal Type   (Bit-rate)              Value (Bytes/Sec)

(IEEE Floating point)

-----------   -----------             ------------

DS0  (0.064 Mbps)              0x45FA0000

DS1  (1.544 Mbps)              0x483C7A00

E1  (2.048 Mbps)              0x487A0000

DS2  (6.312 Mbps)              0x4940A080

E2  (8.448 Mbps)              0x4980E800

Ethernet  (10.00 Mbps)              0x49989680

E3  (34.368 Mbps)             0x4A831A80

DS3  (44.736 Mbps)             0x4AAAA780

STS-1  (51.84 Mbps)              0x4AC5C100

Fast Ethernet  (100.00 Mbps)             0x4B3EBC20

E4  (139.264 Mbps)            0x4B84D000

OC-3/STM-1  (155.52 Mbps)             0x4B9450C0

OC-12/STM-4  (622.08 Mbps)             0x4C9450C0

GigE  (1000.00 Mbps)            0x4CEE6B28

OC-48  (2488.32 Mbps)            0x4D9450C0

OC-192  (9953.28 Mbps)            0x4E9450C0

10GigE-LAN  (10000.00 Mbps)           0x4E9502F9

[Page 9]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

2.3.3. Shared Risk Link Group Identifier (SRLG):

SRLGs to which the link is a member.  This information is manually

configured on the DWDM systems by the service providers. Used for

diverse path computation.

It's quite easy to see the distinction between this type of information (which relates to physical facilities, and hence native to the WDM domain) versus stuff like encoding type. I think the other stuff should be removed.

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|0|         Type = TBD          |   4 * No. of SRLGs in link    |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                  Shared Risk Link Group Value                 |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                        ............                           |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                  Shared Risk Link Group Value                 |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

.  Type: 15 bits = TBD

.  Length: 16 bits = 4 * No. of SRLGs in link

.  Shared Risk Link Group Value: 32 bits

List as many SRLGs as apply.

2.3.4. Wavelength

The wavelength being used by the WDM system to transport the

component link.  Note: this is needed for a transparent system, but

of questionable use for an opaque system.

What's the definition of a transparent and opaque system here?

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|0|         Type = TBD          |          Length = 4           |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                          Wavelength                           |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

.  Type: 15 bits = TBD

.  Length: 16 bits = 4

.  Wavelength: 32 bits

Local identifier for wavelength on which the WDM system will

transmit the signal from the link.

What precisely is the use of this information?

[Page 10]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

2.3.5. Bit Error Rate (BER) Estimate

This TLV provides an estimate of the BER for the component link.

The bit error rate (BER) is the percentage of bits that have errors

relative to the total number of bits received in a transmission,

usually expressed as ten to a negative power. For example, a

transmission might have a BER of 10 to the minus 6, meaning that,

out of 1,000,000 bits transmitted, one bit was in error. The BER is

an indication of overall link quality.

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|0|         Type = TBD          |          Length = 4           |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                   Reserved                    |     BER       |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

.  Type: 15 bits = TBD

.  Length: 16 bits = 4

.  Reserved: 24 bits

Must be set to zero on transmit and ignored on receive.

.  BER: 8 bits

The exponent from the BER representation described above.  For

example, if the BER is 10 to the minus X, the BER field is set

to X.

How is the BER calculated? Also, it seems some of these parameters are relatively static (e.g., SRLG) while some are highly dynamic (BER). Shouldn't the dynamic parameters be indicated using an asynchronous notify mechanism from the WDM to the OXC?

2.3.6. Optical Protection

Whether the WDM system protects the link internally.  This

information can be used as a measure of quality of the link.  It may

be advertised by routing and used by signaling as a selection

criterion as described in [GMPLS].

I'm curious, is this really a feature in any existing WDM system? Also, if this feature exists, should it be visible to OXCs, since they may anyway do 1+1, etc at their layer?

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|0|         Type = TBD          |          Length = 4           |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                   Reserved                        | Link Flags|

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

[Page 11]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

.  Type: 15 bits = TBD

.  Length: 16 bits = 4

.  Reserved: 24 bits

Must be set to zero on transmit and ignored on receive.

.  Link Flags:  6 bits

Indicates supported link protection type.  These link flags are

intended to be consistent with those defined in [GMPLS].

The following flags are defined:

.  0x20  Enhanced

Indicates that a protection scheme that is more reliable than

Dedicated 1+1 should be used, e.g., 4 fiber BLSR/MS-SPRING.

.  0x10  Dedicated 1+1

Indicates that a dedicated link layer protection scheme,

i.e., 1+1 protection, should be used to support the LSP.

.  0x08  Dedicated 1:1

Indicates that a dedicated link layer protection scheme,

i.e., 1:1 protection, should be used to support the LSP.

.  0x04  Shared

Indicates that a shared link layer protection scheme, such as

1:N protection, should be used to support the LSP.

.  0x02  Unprotected

Indicates that the LSP should not use any link layer

protection.

.  0x01  Extra Traffic

Indicates that the LSP should use links that are protecting

other (primary) traffic.  Such LSPs may be preempted when the

links carrying the (primary) traffic being protected fail.

[Page 12]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

2.3.7. Span Length:

Distance of fiber in WDM system.  May be used as a routing metric or

to estimate delay.

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|0|         Type = TBD          |          Length = 4           |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                         Span Length                           |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

.  Type: 15 bits = TBD

.  Length: 16 bits = 4

.  Span Length: 32 bits

Length of WDM span in meters.

2.3.8. Administrative Group (Color)

The administrative group (or Color) to which the component link

belongs.

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|0|         Type = TBD          |          Length = 4           |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                     Administrative Group                      |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

This is another parameter that shouldn't be in a WDM system. It simply doesn't belong there because admin group has no relevance to the physical link that the WDM terminates. It applies only to an OXC-to-OXC link. For example, consider the case where OXC1 is connected to WDM1, but unknown to the WDM system, OXC1 is replaced by another OXC connecting to it. The admin group can change for the OXC-to-OXC links using WDM1. Should the WDM administrator worry about such changes? It also introduces a complex situation where the admin group info is conveyed by the OXC administrators to the WDM administrators only to be sent back using OLI to the OXCs.

.  Type: 15 bits = TBD

.  Length: 16 bits = 4

.  Administrative Group: 32 bits

A 32 bit value.

2.4. Fault Management

Fault management consists of three major functions:

1. Fault Detection

[Page 13]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

2. Fault Localization

3. Fault Notification

The actual Fault Detection mechanisms are the responsibility of the

individual nodes and are not specified as part of this protocol.

Fault detection mechanisms may include such things as bit error rate

(BER) exceeding a threshold, loss of signal (LOS) and certain SONET-

level errors.

The fault notification and localization procedure is essentially the

same as in the current version of LMP, however, it is executed at

two levels in the extended OXC-WDM LMP.

I can see fault notification (between WDM and OXC) as a function, but I'm not sure what you mean by fault localization here. Are two WDM systems talking to each other to localize a fault? (since you're saying this is similar to LMP fault localization).

OXCs continue to execute the OXC-to-OXC fault localization as

currently specified.  The main difference is that the WDM system may

initiate the process (both downstream and upstream).  It is

important to note that the OLS does not participate in end-to-end

fault localization as described in [LMP].

There is no need here even to refer to LMP fault localization procedures. It's only confusing and doesn't contribute to this discussion. Indeed, LMP may not even be running.

The WDM system may also execute its own fault localization process

that may allow it to determine the location of the fault much more

specifically than the OXCs can.  For example, the WDM transmission

system may be able to pinpoint the fault to a particular amplifier

along a set of fibers that can span 1000's of kilometers.

To report individual link failure and recovery conditions, LMP-WDM

uses a new message called the ChannelStatus Message. The

ChannelStatus Message is described below.

2.4.1. ChannelStatus Message (MsgType = TBD)

The ChannelStatus message is sent over the control channel and is

used to report the operational status of a data link (port or

component link).  A ChannelStatus Message must be sent after

receiving a ChannelActive message.  While channels are active, a

ChannelStatus Message must also be sent every time that the status

changes.  A channel status message must also be sent if a

ChannelStatusReq Message is received.

A neighboring node that receives a ChannelStatus message MUST

respond with a ChannelStatusAck message.  The format is as follows:

Can't this description be more explicit, i.e., the Status message is always sent by the WDM. The ack is always sent by the OXC.

<ChannelStatus Message> ::= <Common Header> <ChannelStatus>

The format of the ChannelStatus object is as follows:

[Page 14]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                           MessageId                           |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                                                               |

//                        (Status TLVs)                       //

|                                                               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

MessageId:  32 bits

When combined with the Local TE Link Id in the common header of

the received packet, the MessageId field uniquely identifies a

message.  This value is incremented and only decreases when the

value wraps.  This is used for message acknowledgement in the

ChannelStatusAck message.

The ChannelStatus message must include at least one Status TLV.  To

specify a status for the whole TE Link, use the group status TLV and

link group 0xFFFFFFFF.

TE link?

2.4.1.1. Channel Status TLV

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|0|           TBD               |             Length            |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                     Local Interface Id                        |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|   Condition   |                  (Reserved)                   |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

The Channel Status TLV is non-negotiable.

Length:  16 bits

The Length is in bytes (see LMP TLV format).

Local Interface Id:  32 bits

This is the local Interface Id (either Port Id or Component

Interface Id) of the data link that has failed.  This is within

the scope of the TE Link Id.

Please get rid of the TE link notion. It's confusing.

[Page 15]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

Condition:  8 bits

Status Condition:

Value    Condition                   Description

-----    ---------                   -----------

1     Signal Okay   Port is operational.

(OK)

2    Signal Degrade  A soft failure caused by a BER

(SD)       exceeding a preselected threshold.  The

specific BER used to define the

threshold is may be configured, but is

typically in the range of 10-5 to 10-9.

Why should the threshold be configured in the WDM? Why can't the BER be simply reported and the OXC decide whether it's within a threshold or not? This is another instance where semantics at the OXC layer are imported into WDM and then exported back.

3     Signal Fail   A hard signal failure including (but

(SF)       not limited to) loss of signal (LOS),

loss of frame (LOF), Line AIS, or a BER

(BIP-8 measure through B1/B2) exceeding

a specified value.

2.4.1.2. Group Status TLV

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|0|           TBD               |             Length            |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                        Link Group Id                          |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|   Condition   |               (Reserved)                      |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

The Group Status TLV is non-negotiable.

Length:  16 bits

The Length is in bytes (see LMP TLV format).

Link Group Id:  32 bits

This is the Link Group ID.

[Page 16]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

Condition:  8 bits

Status Condition:

Value    Condition                   Description

-----    ---------                   -----------

1     Signal Okay   Port is operational.

(OK)

2    Signal Degrade  A soft failure caused by a BER

(SD)       exceeding a preselected threshold.  The

specific BER used to define the

threshold is may be configured, but is

typically in the range of 10-5 to 10-9.

3     Signal Fail   A hard signal failure including (but

(SF)       not limited to) loss of signal (LOS),

loss of frame (LOF), Line AIS,

Equipment failure, or a BER (BIP-8

measure through B1/B2) exceeding a

specified value.

See comments on link group.

2.4.2. ChannelStatusAck Message (MsgType = TBD)

The ChannelStatusAck message is used to indicate that all of the

status TLVs in the ChannelStatus message have been received without

error.

The format is as follows:

<ChannelStatusAck Message> ::= <Common Header> <ChannelStatusAck>

The ChannelStatusAck object has the following format:

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                          MessageId                            |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                      Remote TE Link Id                        |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

MessageId:  32 bits

This is copied from the ChannelStatus message being

acknowledged.

Remote TE Link Id: 32 bits

This is copied from the Common Header of the ChannelStatus

message being acknowledged.

Again, I'm not sure what the TE link ID means here. Is this individual link ID or a group ID? Call it physical link ID if it refers to an individual link.

[Page 17]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

2.4.3. ChannelStatusReq Message (MsgType = TBD)

The ChannelStatusReq message is sent over the control channel and is

used to request the status of one or more data link(s) (port or

component link).

A neighboring node that receives a   ChannelStatusReq message MUST

respond with a  ChannelStatus message.  The format is as follows:

< ChannelStatusReq Message> ::=

<Common Header> < ChannelStatusReq>

The format of the   ChannelStatusReq object is as follows:

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                           MessageId                           |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                                                               |

//                        (Entity TLVs)                        //

|                                                               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

MessageId:  32 bits

When combined with the Local TE Link Id in the common header of

the received packet, the MessageId field uniquely identifies a

message.  This value is incremented and only decreases when the

value wraps.  This is used for message acknowledgement in the

ChannelStatusReqAck message.

A  ChannelStatusReq Message may include zero or more Entity TLVs.  If

no Entity TLVs are included, the receiving node must report on all

component links within the TE link.

2.4.3.1. Channel Entity TLV

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|0|           TBD               |             Length            |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                     Local Interface Id                        |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

The Channel Status TLV is non-negotiable.

Length:  16 bits

[Page 18]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

The Length is in bytes (see LMP TLV format).

Local Interface Id:  32 bits

This is the local Interface Id (either Port Id or Component

Interface Id) of the data link for which status is requested.

This is within the scope of the TE Link Id.

2.4.3.2. Group Entity TLV

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|0|           TBD               |             Length            |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                        Link Group Id                          |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

The Group Status TLV is non-negotiable.

Length:  16 bits

The Length is in bytes (see LMP TLV format).

Link Group Id:  32 bits

The Link Group ID for which status is requested.  This is

within the scope of the TE Link Id.

So, how does fault notification work?

2.5. Trace Monitoring

The trace monitoring features described in this section, allow the

PXC to do basic trace monitoring on circuits by using the

capabilities on the attached OLSs

. An OLS Client to requests the OLS to monitor a link for a

specific pattern in the overhead using the TraceMonitorReq

Message.  An example of this overhead is the SONET Section

Trace message transmitted in the J0 byte.  If the actual trace

message does not match the expected trace message, the OLS must

report the mismatch condition.

. An OLS client may request the value of the current trace

message on a given port using the TraceReq Message.

2.5.1. TraceMonitor Message (MsgType = TBD)

[Page 19]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

The TraceMonitor message is sent over the control channel and is

used to request an OLS to monitor a one or more component links for

a specific trace value.  An OLS must respond to a TraceMonitor

message with either a TraceMonitorAck or TraceMonitorNack Message.

<TraceMonitor Message> ::= <Common Header> <TraceMonitor>

The format of the TraceMonitor object is as follows:

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                           MessageId                           |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                                                               |

//                         (Trace TLVs)                        //

|                                                               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

MessageId:  32 bits

When combined with the Local TE Link Id in the common header of

the received packet, the MessageId field uniquely identifies a

message.  This value is incremented and only decreases when the

value wraps.  This is used for message acknowledgement in the

ChannelStatusAck message.

The ChannelStatus message must include at least one Status TLV.  To

specify a status for the whole TE Link, use the group status TLV and

link group 0xFFFFFFFF.

2.5.1.1. SONET Section Trace TLV

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|0|           TBD               |             Length            |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                     Local Interface Id                        |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                          Trace Message                        |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

The Channel Status TLV is non-negotiable.

Length:  16 bits

The Length is in bytes (see LMP TLV format).

Local Interface Id:  32 bits

[Page 20]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

This is the local Interface Id (either Port Id or Component

Interface Id) of the data link for which the trace monitoring

is requested.  This is within the scope of the TE Link Id.

Trace Message:  32 bits

32 bit SONET section trace value.

2.5.1.2. Trace TLV

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|0|           TBD               |             Length            |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                     Local Interface Id                        |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|           Trace Type          |          Trace Length         |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                                                               |

//                         Trace Message                       //

|                                                               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

The Channel Status TLV is non-negotiable.

Length:  16 bits

The Length is in bytes (see LMP TLV format).

Local Interface Id:  32 bits

This is the local Interface Id (either Port Id or Component

Interface Id) of the data link for which the trace monitoring

is requested.  This is within the scope of the TE Link Id.

Trace Type: 16 bits

The type of the trace message:

1 – SONET Section Trace (J0 Byte)

2 – SONET Path Trace (J1 Byte)

3 – SDH Section Trace (J0 Byte)

4 – SDH Path Trace (J1 Byte)

Why would the WDM system look at the path trace? The idea of path trace is to trace an entire path.

Other types TBD.

Trace Length:  16 bits

The Length in bytes of the trace message provided.

[Page 21]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

Trace Message:

Expected message.  The valid length and value are determined by

the specific technology (e.g., SONET or SDH) and are beyond the

scope of this document.  The message must be padded with zeros

to a 32-bit boundary, if necessary.

2.5.2. TraceMonitorAck Message (MsgType = TBD)

The TraceMonitorAck message is used to indicate that all of the

Trace TLVs in the TraceMonitor message have been received and

processed correctly.

The format is as follows:

<TraceMonitorAck Message> ::= <Common Header> <TraceMonitorAck>

The TraceMonitorAck object has the following format:

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                          MessageId                            |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                      Remote TE Link Id                        |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

MessageId:  32 bits

This is copied from the ChannelStatus message being

acknowledged.

Remote TE Link Id: 32 bits

This is copied from the Common Header of the ChannelStatus

message being acknowledged.

2.5.3. TraceMonitorNack Message (MsgType = TBD)

The TraceMonitorNack message is used to indicate that one or more of

the Trace TLVs in the TraceMonitor message was not processed

correctly.  This could be because the trace monitoring requested is

not supported or there was an error in one of the values.

What error? A trace is just a collection of bits as defined here. What does it mean by an error in this case?

The format is as follows:

<TraceMonitorNack Message> ::= <Common Header> <TraceMonitorNack>

The TraceMonitorNack object has the following format:

[Page 22]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                          MessageId                            |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                      Remote TE Link Id                        |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                                                               |

//                   (Rejected Trace TLVs)                     //

|                                                               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

MessageId:  32 bits

This is copied from the ChannelStatus message being

acknowledged.

Remote TE Link Id: 32 bits

This is copied from the Common Header of the ChannelStatus

message being acknowledged.

Rejected Trace TLVs: 32 bits

Trace TLVs that were not accepted.  Copied from TraceMonitor

message.  If none are included, it means that all Trace TLVs

are rejected.

2.5.4. TraceMismatch Message (MsgType = TBD)

The TraceMismatch message is sent over the control channel and is

used to report a trace mismatch on a component link for which trace

monitoring was requested.

A neighboring node that receives a TraceMismatch message MUST

respond with a TraceMismatchAck message.  The format is as follows:

I think in all these descriptions, you can be explicit about which node (OXC or WDM) sends what message, since the roles are fixed.

<TraceMismatch Message> ::= <Common Header> <TraceMismatch>

The format of the TraceMismatch object is as follows:

[Page 23]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                           MessageId                           |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                                                               |

//                     Local Interface Ids                     //

|                                                               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

MessageId:  32 bits

When combined with the Local TE Link Id in the common header of

the received packet, the MessageId field uniquely identifies a

message.  This value is incremented and only decreases when the

value wraps.  This is used for message acknowledgement in the

ChannelStatusAck message.

Local Interface Id:  32 bits per Id

This is the local Interface Id (either Port Id or Component

Interface Id) of the data link that has a trace mismatch.  This

is within the scope of the TE Link Id.  Multiple Local

Interface Ids may be reported in the same message.

2.5.5. TraceMismatchAck Message (MsgType = TBD)

The TraceMismatchAck message is used to acknowledge receipt of a

TraceMismatch message.

The format is as follows:

<TraceMismatchAck Message> ::= <Common Header> <TraceMismatchAck>

The TraceMismatchAck object has the following format:

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                          MessageId                            |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                      Remote TE Link Id                        |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

MessageId:  32 bits

This is copied from the ChannelStatus message being

acknowledged.

Remote TE Link Id: 32 bits

[Page 24]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

This is copied from the Common Header of the ChannelStatus

message being acknowledged.

2.5.6. TraceReq Message (MsgType = TBD)

The TraceReq message is sent over the control channel and is used to

request the current trace value of indicated component links.

A node that receives a TraceReq message MUST respond with a

TraceReport message.  The format is as follows:

<TraceReq Message> ::= <Common Header> <TraceReq>

The format of the TraceReq object is as follows:

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                           MessageId                           |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                                                               |

//                        (Entity TLVs)                        //

|                                                               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

MessageId:  32 bits

When combined with the Local TE Link Id in the common header of

the received packet, the MessageId field uniquely identifies a

message.  This value is incremented and only decreases when the

value wraps.  This is used for message acknowledgement in the

TraceReport message.

A  TraceReq Message may include zero or more Entity TLVs (as

described in Section 2.4.3).  If no Entity TLVs are included, the

receiving node must report on all component links within the TE

link.

2.5.7. TraceReport Message (MsgType = TBD)

The TraceReport message is sent over the control channel after

receiving a TraceReq message.

<TraceReport Message> ::= <Common Header> <TraceReport>

The format of the TraceReport object is as follows:

[Page 25]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                           MessageId                           |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                                                               |

//                         (Trace TLVs)                        //

|                                                               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

MessageId:  32 bits

This is copied from the TraceReq message being acknowledged.

The TraceReport message must include a Trace TLV (as described in

Section 2.5.1) for each link requested.

3. Security Considerations

The security considerations are the same as in [LMP].

[Page 26]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

4. References

[GMPLS]       Berger, L., Ashwood-Smith, Peter, editors,

"Generalized MPLS - Signaling Functional Description",

Internet Draft, draft-ietf-mpls-generalized-signaling-

02.txt, (work in progress), March 2001.

[Bra96]       Bradner, S., "The Internet Standards Process --

Revision 3," BCP 9, RFC 2026, October 1996.

[DBC00]      Drake, J., Blumenthal, D., Ceuppens, L., et al.,

"Interworking between Photonic (Optical) Switches and

Transmission Systems over Optical Link Interface (OLI)

using Extensions to LMP", OIF Contribution

oif2000.254, (work in progress), November 2000.

[KRB00]       Kompella, K., Rekhter, Y., Berger, L., "Link Bundling

in MPLS Traffic Engineering," Internet Draft, draft-

kompella-mpls-bundle-02.txt, (work in progress), July

2000.

[KRB00a]      Kompella, K., Rekhter, Y., Banerjee, A., et al, "OSPF

Extensions in Support of Generalized MPLS," Internet

Draft, draft-kompella-ospf-extensions-00.txt, (work in

progress), July 2000.

[LMP]         Lang, J., Mitra, K., Drake, J., Kompella, K., Rekhter,

Y., Berger, L., Saha, D., Basak, D., Sandick, H.,

Zinin, A., "Link Management Protocol (LMP)", Internet

Draft, draft-ietf-mpls-lmp-01.txt, (work in progress),

November 2000.

[OLI]         Fredette, A., Editor, "Optical Link Interface

Requirements", Internet Draft, draft-many-oli-reqts-

00.txt, (work in progress), June 2001.

[SDH]         ITU-T G.707, "Network node interface for the

synchronous digital hierarchy (SDH)", 1996.

[SONET]       GR-253-CORE, "Synchronous Optical Network (SONET)

Transport Systems: Common Generic Criteria", Telcordia

Technologies, Issue 3, September 2000

[T.50]        ITU-T T.50, "International Reference Alphabet (IRA)

(formerly International Alphabet No. 5 or IA5)

Information technology 7-bit coded character set for

information interchange.", 1992.

[Page 27]

Internet Draft       draft-many-oli-reqts-00.txt            July 2001

5. Author's Addresses

Andre Fredette                          Ed Snyder

PhotonEx Corporation                    PhotonEx Corporation

8C Preston Court                        8C Preston Court

Bedford, MA  01730                      Bedford, MA  01730

email: fredette@photonex.com            email: esnyder@photonex.com

Jagan Shantigram                        Jonathan P. Lang

PhotonEx Corporation                    Calient Networks

8C Preston                              Court25 Castilian Drive

Bedford, MA  01730                      Goleta, CA 93117

email: jagan@photonex.com               email: jplang@calient.net

John Drake                              Gopala Tumuluri

Calient Networks                        Calient Networks

5853 Rue Ferrari                        5853 Rue Ferrari

San Jose, CA 95138                      San Jose, CA 95138

email: jdrake@calient.net               email: krishna@calient.net

Rohit Goyal                             Stuart Brorson

Axiowave Networks                       Axiowave Networks

100 Nickerson Road                      100 Nickerson Road

Marlborough, MA 01752                   Marlborough, MA 01752

email: rgoyal@axiowave.com              email: sdb@axiowave.com

Ram Krishnan                            W. L. Edwards

Axiowave Networks                       iLambda Networks

100 Nickerson Road                      Aspen, CO

Marlborough, MA 01752                   email: texas@ilambda.com

email: ram@axiowave.com

Yong Xue                                John Yu

UUNET/WorldCom                          Zaffire, Inc

22001 Loudoun County Parkway            2630 Orchard Parkway

Ashburn, VA 20148                       San Jose, CA 95134

email: yxue@uu.net                      email: jzyu@zaffire.com

Sudheer Dharanikota

Nayna Networks, Inc.

157 Topaz Drive,

Milpitas, CA 95035

email: sudheer@nayna.com

[Page 28]