## Slide 1: GMPLS Interoperability Test Event Results and Recommendations
Ashok Narayanan, Cisco Systems ashokn@cisco.com
Ben Schultz, UNH Interoperability Lab schultz@iol.unh.edu
July 29, 2026

## Slide 2: Agenda
Overview of GMPLS Interoperability Test Event
Issues for CCAMP WG to consider
Issues for vendors to consider
Conclusion
Acknowledgements

## Slide 3: Overview of GMPLS Interop
Held at UNH Interoperability Lab
Staging for GMPLS demo at NGN 2002
Organized by The MPLS Forum
Participants
  Equipment Implementations
  Routers: Cisco, Juniper
  Switch: Sycamore
  Emulated Implementations
  Stacks: Netplane, DCL
  Test Eqpt: Agilent, NetTest

## Slide 4: Overview of GMPLS Interop

## Slide 5: Results of GMPLS Interop
Demonstrated multi-vendor LSPs
LSPs signaled using GMPLS RSVP/TE
  Statically routed (no OSPF/TE, no LMP)
  Numbered links
  Single control Ethernet network
Sent data traffic where possible
Strict, some loose ERO support tested
Details in Test Plan & Results Whitepaper
  http://www.mplsforum.org/NGNevent.html

## Slide 6: WG Issues – ResvConf address
OOB ResvConf message addressed to….?
  Confirm Requester (as in RFC2205)
    Supports ResvConf to non-participant in LSP signaling
    ResvConf can propagate without LSP state
    Requires integrity keys between endpoints
  Next-hop (like PathTear)
    Doesn’t require extra integrity keys
    ResvConf cannot propagate without LSP state
    ResvConf must be to participant in LSP signaling
Recommendation: Next-hop
  Isomorphic to ResvError
  Requires standards note

## Slide 7: Vendor Issues – Port label
What is the port label value for FSC/LSC?
  Draft specifies label mapping is private
  Vendors “agreed” on interface-index (what about numbered?)
  Remotelocal mapping of label same as interface-index mapping
  Vendors viewed this as a global rule
Result: Must use private mapping
  Label mapping independent of interface-index mapping
  Vendors should implement remotelocal label mapping
    configured or discovered (LMP)
  No reliance on interface-index mapping or any network-global label mapping rule
  Applies to FSC or LSC, numbered or unnumbered
  Section 3.2.1.1, draft-ietf-mpls-generalized-signaling-09

## Slide 8: Vendor Issues – Signaling address
Out of band signaling: “control” IP address?
  In IF-ID HOP and ERROR objects
  Source and destination address of message
Historically: address of msg output interface
May cause instability during CC changeover
  PHOP “control” address must change for Resv reachability
  Message-IDs invalid across CC change
Recommendation: Use a stable address
  Router-ID is a good candidate
    May need routing (IGP/LMP/static) for reachability
Implementations must receive any ctrl address
  Receiver not responsible for unstable ctrl address

## Slide 9: Vendor Issues - TSpecs
When to generate SONET/SDH TSpecs?
  Interop: draft-ietf-ccamp-gmpls-sonet-sdh-05: for any SONET-encoded LSP. Vendors disagreed.
  Result: draft-ietf-ccamp-gmpls-sonet-sdh-07: Only for TDM switching or special transparency
Should PathError include TSpec?
  RFC2205: <sender_descriptor> optional in Path and PathError, but PathError reflects from Path
  RFC3209: <sender_descriptor> required in Path
  RFC2205: <sender_descriptor> requires both SENDER_TEMPLATE and SENDER_TSPEC
  Result: PathError for LSP must include TSpec

## Slide 10: Vendor issues – Receipt of ERO
Vendors should accept Path messages with or without an ERO
  Receiver nodes – should accept both
  Switch nodes – depends on feature availability
    Without ERO
    With strict ERO only
    With ERO (strict or loose)
    Combinations (e.g. 1 & 2, 1 & 3)
  Switch nodes must clearly document what they do

## Slide 11: Vendor issues - miscellaneous
  Vendors should behave as per spec for:
    Path with or without Label Set
    ResvConfirm support
    SONET label for TDM switching
    SONET TSpec including Profile field
    Session address: Router-ID or other local
    Sender template address: Router-ID or local
    Message-ID Acks: from Router-ID or other
  Vendors should document features that they support for the above

## Slide 12: Conclusion
We tested GMPLS RSVP/TE interoperability
We found a limited set of issues with the draft specifications, as per our test plan
We also provide some implementation recommendations to vendors
Details in Test Plan & Results Whitepaper
  http://www.mplsforum.org/NGNevent.html

## Slide 13: Acknowledgements
MPLS Forum
UNH Interoperability Labs
Agilent Technologies
Cisco Systems
Data Connection Ltd (DCL)
Juniper Networks
NetPlane Systems Inc.
NetTest Inc.
Sycamore Networks