## Slide 1: MPLS & GMPLS Control and management 2 Issues
Avri Doria
Atlanta GA

## Slide 2: 2 issues
Too many ways to control/manage MPLS & GMPLS?
Are MIBS the best choice for
  Configuring
  Provisioning
  Controlling
  a label switch?

## Slide 3: Issue 1: Too many control paths between a (G)MPLS Agent/Controller & Label Switch
MIBS
  The common choice?
Command Line interface (several flavors)
  Always available, always used
GSMP
  Still underutilized
  Current deployment in Korea and Japan
TL -1
Vendor proprietary
SP proprietary
More?

## Slide 4: So?
Changes made by one agent/controller are not communicated to the others.
  If a view of the state of the switch is kept by the agent/controller then state becomes inconsistent
  if state is not kept, is it efficient to retrieve full state for every decision?

## Slide 5: Proposal for issue 1
There should be a requirement that any control or management scheme for GMPLS
  Keep state
  Support notification by the switch of any changes in state made in the managed state.

## Slide 6: Issue 2: Are MIBS the best solution for Configuration and Control of GMPLS?
MIBS can be used to ‘manage’ anything and lots of people can do MIBS
But
GMPLS/MPLS MIBS showing rampant complexity
GMPLS/MPLS MIBS challenging the bounds of scalability
Information flow in GMPLS may be too dynamic for effective management by SNMP

## Slide 7: Another possibility
(Re)consider use of GSMPv3
  It has come a long way in the last few years
  Specialized support for label switches,
    i.e. MPLS support
  Is currently being fitted with GMPLS support
    Label types
    Port types
    OXC transaction models
    OXC Restoration capabilities
    Optical Cross connect support
    Optical Burst Switching support
    Resource Partitioning

## Slide 8: Current Charter
Changes to GSMP necessary for the support of
  optical (non-transparent and all optical)
  SONET/SDH, and
  spatial switching of IP packets,
  L2 frames and TDM data.
GSMP controllers will then be able to control:
  photonic cross- connects (optical-optical),
  transparent optical cross connects (optical-electrical-optical, frame independent)
  opaque cross connects (optical-electrical-optical, SONET/SDH frames)
  traditional TDM switches (all electrical).

## Slide 9: Label types
PS: ATM, Frame Relay, DS1, DS3, E1, E3, MPLS Generic Labels and MPLS FECs
Work in progress:
  Digital Carrier Hierarchy (e.g., DS-1, E1),
  SONET and SDH Hierarchy
    e.g., OC-3, STM-1, VT1.5, VC-12
  PDH labels
  OTN G.709 labels
  Lambdas
  Fibers
  Label Hierarchies and Label Lists

## Slide 10: Port Types
Work in progress to
support the mix of optical signals that can operate over a single fiber.
  wavelengths available per interface
  bit rate per wavelength
  type of fiber
Support various types of transport signal
Support naming of 10s of 1000s of ports

## Slide 11: OXC transaction models
Work in progress to support:
  Parallel
  Serial
  Bulk

## Slide 12: OXC Restoration
Work in Progress:
Support hardware mechanisms e.g. ring restoration
  Non reserved protection links (1:n)
  Dedicated Protection Links (1+1)
Protection triggers

## Slide 13: GSMP WG request to CCAMP WG
Please review
//ietf.org/internet-drafts/draft-ietf-gsmp-reqs-04.txt
Make sure it requires all that is needed.
GSMP meets Thursday 13.00 – 15.00 &
Requirements will be discussed