## Slide 1: GMPLS for Multi-Region Networks
dimitri.papadimitriou@alcatel.be
{martin.vigoureux, emmanual.dotaro}@alcatel.fr
{shiomoto.kohei, oki.eiji, matsuura.nobuaki}@lab.ntt.co.jp
draft-vigoureux-shiomoto-ccamp-gmpls-mrn-00.txt
IETF 55 (Atlanta) - November 2002

## Slide 2: Rationales
Horizontal integration => multi-area w/ single switching capability nodes
Vertical integration => single-area w/ multiple switching capability nodes
  Vertical integration refers to multi-region networks controlled by single GMPLS instance => MRN: ISC1,…, ISCn with at least n >= 2 for N >= 2
Note: FA positioning wrt integration => initial iteration of vertical integration (i.e. w/ single switching capability nodes)

## Slide 3: Rationales
Consider network with L2SC (e.g. Ethernet) + LSC, L2SC only and LSC only LSRs => what a Single GMPLS controller instance brings ?
  decrease interactions & processing complexity (compared to multiple GMPLS instances) and benefits from single addressing/identification space
  n switching capabilities => complexity ~ (n x L) Log (n x N) => pre-selection (control plane) reduces to ~ n Log(n+1) Log ((Log (n+1) +N)
Can only belong to the CCAMP WG since focus on common protocol aspects

## Slide 4: What do we discuss …
FA-based virtual topologies (abstract view of network resources without generating “well-known” overlay complexity)
FA ISC1,…,ISCn <=> TE Metric unicity ?
Adaptation capability - b/w SC (resource capability/ availability and weight for accessing a given switching capability)
LSP Setup: concurrent versus sequential (+ crossing region - switching capability - on a per hop basis)

## Slide 5: But also… as next step ?
Multiplexing several incoming LSP into single tunnel (Multiplexing Point >= 1) => raising issues ranging from mp2p to mp2mp ?
  => common protocol scope ?
Particular Case
  Physical Constraints & TE Link Selection in Hybrid Photonic Networks (HPN) - routing
  Regeneration in HPN (depends either on switching or encoding) => cut through through explicit label control - signalling

## Slide 6: First Conclusion
Suitability ? Target is NOT exhaustive and fully “universal MPLS” but applicability of common protocols for multiple SC environments
Justification ? Enabling GMPLS collaborative mechanisms by mean of common protocol enhancements
Ensure backward compatibility w/ current GMPLS protocol suite by guaranteeing handled and limited complexity
… we just deliver some alternatives for doing so