## Slide 1: Recovery Terminology for GMPLS draft-ietf-ccamp-gmpls-recovery-terminology-01.txt Analysis of GMPLS-based Recovery Mechanisms draft-papadimitriou-ccamp-gmpls-recovery-analysis-03.txt GMPLS Recovery Functional Specification draft-bala-gmpls-recovery-functional-01.txt
Protection & Restoration Design Team - CCAMP WG
IETF 55 - Atlanta November’02

## Slide 2: Effort Positioning, Status & Timing
Terminology
Functional Specification (*)
Analysis
GMPLS Protocol Specification
draft-ietf-ccamp-gmpls-recovery-terminology-01.txt
draft-papadimitriou-ccamp-gmpls-recovery-analysis-03.txt
draft-bala-gmpls-recovery-functional-01.txt
first version to be issued (after agreement on *)
April’02
July’02
March’02
Aug’02
March’02 (closed)
Nov’02 (closed ~ Aug’02)
Nov’02 (closed ~ Nov’02 ?)

## Slide 3: Thanks…
P&R Design Team:
Deborah Brungard
Sudheer Dharanikota
Jonathan Lang
Guangzhi Li
Eric Mannie
Dimitri Papadimitriou
Bala Rajagopalan
Yakov Rekhter

## Slide 4: Some words about the Analysis I-d
Part 1. Recovery phase analysis
  (Phase 1: Failure detection)
  Phase 2: Failure localization/isolation
  Phase 3: Failure notification
  Phase 4: Recovery (protection/restoration)
  Phase 5: Reversion (normalization)
Part 2. Focus on Phase 5
  Recovery mechanisms and schemes
  Provides classification of the restoration schemes
Part 3. Focus on Phase 6 - Reversion (Normalization)
Part 4. Horizontal & vertical hierarchy, Escalation strategies and Disjointness
Part 5. Dimensions for recovery Scheme/Strategy analysis: fast convergence, efficiency, robustness & resource optimization

## Slide 5: Recovery Mechanisms Applicability
-----------------------------------------------------------------------
| Path Search (computation and selection)
-----------------------------------------------------------------------
| Pre-planned (Pre-signalling)| Dynamic
-----------------------------------------------------------------------
| | - faster recovery | Does not apply
| | - less flexible |
| 1 | - less robust |
| | - most resource consuming |
Path | | => LSP protection |
Setup ---------------------------------------------------------------
| | - relatively fast recovery | Does not apply
| | - relatively flexible |
| 2 | - relatively robust |
| | - resource consumption |
| | depends on sharing degree |
| | => recovery LSP activation |
---------------------------------------------------------------
| | - relatively fast recovery | - less faster (computation)
| | - more flexible | - most flexible
| 3 | - relatively robust | - most robust
| | - less resource consuming | - least resource consuming
| | (depends on sharing degree) | => LSP re-routing
| | => reservation + activation |
------------------------------------------------------------------------

## Slide 6: Some words about the functional I-d
Version -01.txt submitted
Details the protocol mechanisms (message exchange) and information to be carried to implement these mechanisms
Deliver separately a protocol (message oriented) specification covering the “analyzed” recovery mechanisms

## Slide 7: Some words about the functional I-d
Span (Link) Protection
  Unidirectional 1+1 dedicated protection
  Bi-directional 1+1 dedicated protection
  Dedicated 1:1 protection with Extra Traffic
  Shared M:N protection with Extra Traffic
End-to-End (LSP/LSP segment) Recovery
  Unidirectional 1+1 dedicated protection
  Bi-directional 1+1 dedicated protection
  Dedicated 1:1 recovery with Extra Traffic
  Shared M:N recovery with Extra Traffic
Shared Meshed Recovery
Reversion and other Administrative Procedure

## Slide 8: Issues and Discussion
1) Bulk Recovery
2) Shared Meshed Recovery
3) Reversion

## Slide 9: Bulk LSP Recovery on Link failure
In case of (component) link failure of a TE Link carrying numerous LSPs
Bundle notification messages does not need additional extension if within the same Interface-ID TLV (Extended IF_ID Error_Spec)
Master for the affected LSPs may be located at each side of the TE link => the two masters may compete for the same component link (within the same TE link) resource for recovering these LSPs
However, they may (even prior to the failure) agree on which (common) recovery link these LSPs will be recovered otherwise some fragmentation of the TE link components usage may occur

## Slide 10: Shared Meshed Recovery & related
1. Shared Bandwidth:
  Existing sub-TLVs: Max LSP Bandwidth, Max Reservable Bandwidth and Unreserved Bandwidth
  New sub-TLV: including Sharable Bandwidth for Recovery R[i] (initial value max_R[i]) and Bandwidth committed for (shared) Recovery r[i]
  => Shared recovery ratio per TE Link = (R[i] + r[i]) / r[i]
2. Shared Bandwidth and Disjointness:
  Number of SRLG (and optionally list of SRLG) recoverable
  Sharable/Shared Bandwidth per (group of) SRLG
3. Admission Control:
  send the Explicit Route of the working LSP over the recovery LSP
  not impacting on diversity (lookup in the sub-objects)
Next step

## Slide 11: Reversion
Optional due to potential second hit during to the reversion switching operation
Turn-on/-off (default behaviour settable per policy) either through signalling or policy
Reversion operation
  uses exactly the same LSP as the one previously under failure (default behaviour)
  implies “testing” the LSP (using Admin_Status) before reversion switching
  uses the “bridge and switch” a.k.a “make-before-break”
Keep possibility (e.g. policy or signalling) to clear out the resources on intermediate nodes if reversion switching not possible

## Slide 12: What is the Next Step ?
Terminology
Functional Specification
Analysis
GMPLS Protocol Specification
draft-ietf-ccamp-gmpls-recovery-terminology-01.txt
draft-bala-gmpls-recovery-functional-01.txt
March’02
July’02
Depending on the working group consensus
First phase achievement (~ protocol specification)
Next report ~ dec’02/jan’03 - Deadline 3q’03 to finalize first phase (including protocol specification)
draft-papadimitriou-ccamp-gmpls-recovery-analysis-03.txt
Aug’02
Nov’03 (first phase closed)

## Slide 13: Backup Slide

## Slide 14: Restoration Mechanisms Classification
(1) Route Computation ---> On-demand
|
--> Pre-Computed
|
(2) Signalling ---> On-demand
|
--> Pre-Signaled
|
(3) Resource Selection ---> On-demand
|
--> Pre-Selected
|
(4) Resource Allocation
|
v
Equivalent to Control
plane driven Protection
Impacts the label assignment process - several solutions feasible