## Slide 1: Mobile IP, PMIP, FMC, and a little bit more
Charlie Perkins
Futurewei

## Slide 2: Mobile IPv6 protocol overview
Seamless Roaming: Mobile Node appears “always on” home network
Routing Prefix from local Router Advertisement
Address autoconfiguration  care-of address
Binding Updates  home agent & correspondent nodes
  (home address, care-of address, binding lifetime)
Local Router
charliep@nokia.com
Home Agent
correspondent node
with binding
correspondent node

## Slide 3: Mobile IPv4 protocol overview
Seamless Roaming: Mobile Node appears “always on” home network
Foreign Agent supplies Care-of Address in Agent Advertisement
Or, MN address allocation  care-of address
Registration Request  home agent
  (home address, care-of address, registration lifetime)
Foreign Agent
135.136.137.1
Home Agent
correspondent node

## Slide 4: Proxy Mobile IP (PMIP: RFC 5213)
LMA: the home agent
MAG: the foreign agent
UE: the mobile node
CN: the correspondent node
Main idea: run Mobile IP
without requiring any changes
to the mobile node.
Originally envisioned for a
single network domain
UE thinks MAG always has the same
CoA and even MAC address

## Slide 5: Hierarchical Mobile IP (HMIP: RFC 5380)
UE: the mobile node
MAP: Mobility Access Point
Main idea: hide local
movement in MAP domain

## Slide 6: FMIP (RFC 5568): Smooth/Fast/Seamless Handover
Smooth handover == low loss
Fast handover == low delay [30 ms?]
  Can router pre-empt Duplicate Address Detection??
Seamless handover:
  Fast [localized context transfer via HI and HAck]
  Smooth [buffering]
PAR
NAR

## Slide 7: FMC terminology
“Fixed”
  Fixed means that the access network is DSL
  Or, maybe femtocell
  Device is not really “fixed” at all!
“Mobile”
  A UE (a device managed by a 3GPP network operator)
“Convergence”
  Extend 3GPP policy requirements to WLAN e.g.
Fixed Mobile Convergence
  Mostly, bringing BBF into 3GPP compliance
  But, described as a way of extending user experience
  But, all the changes are on the BBF side

## Slide 8: Why FMC?
Mobile applications demand more and more bandwidth;
Cellular network becoming the bottle-neck
Cellular network operators want to offload the data traffic to the fixed broadband (FBB) network via WLAN/Home (e)NodeB access;
Operators must employ mechanisms to manage the subscriber’s service over both mobile and FBB network, that is FMC.
FMC based on subscribers’ and operators’ requirements.

## Slide 9: Architecture of FMC
The fixed broadband network must partner with the mobile network to perform AAA and acquire the policies for the mobile subscriber.
Fixed Network
M AAA
PDN GW
ePDG
Internet Service
Mobile Network
Operator Service
F AAA
BPCF
PCRF
SGW
BNG
AN
eNB
UE
UE
Femto
WiFi AP
RG

## Slide 10: Key issues in FMC
UE identification in FBB network
Femto Access Point (FAP) Management
Device type identification
Carrier Grade NAT (CGN) related issues
UE mobility in FBB network
Flow mobility between different interfaces

## Slide 11: Issue 1: UE identification FBB network
Key requirements:
  In FMC scenario, the policy control must be based on per-UE granularity.
  Efficient packet inspection deployment
Issue: Limitations with BNG implementations for per-UE granularity enforcement due to address sharing with NAT in RG, in case 2 and 4.
Fixed Network
PDN GW
Mobile Network
Operator Service
SGW
BNG
UE
UE
RG
RG NAT
Mobile UE with mobile-routed traffic and no NAT in RG
Mobile UE with mobile-routed traffic with NAT in RG
Mobile UE with offloaded traffic and no NAT in RG
Mobile UE with offloaded traffic with NAT in RG
Internet Service

## Slide 12: Issue 2: Femtocell AP Management
Key requirements:
  Inter-operators subscribers policy exchange (the private and public addressing which rely on NA(P)T, must be coordinated cross operators);
  Femtocell AP must be identified for management.
Issues:
  Binding the port number after NA(P)T for special Femtocell AP is needed;
  Binding the FAP’s Public IPv4 address and the UE’s inner-IPv4 address is needed.
Fixed Network
PGW
Internet Service
BPCF
UE
FAP
RG
BNG
SeGW
PCRF
FAP-GW
MME/SGW
Mobile Network
Private IP
Inner IP assigned by Mobile Network
Public
IP +Port
(NAPT)
IPSec Tunnel
MME Mobility Management Entity

## Slide 13: Issue 3: Device type identification
Key requirements:
  Only special traffic from special devices, such as mobile phone, need policy control and management. For example, 3GPP service from mobile phone.
Issue:
  In the current WiFi network, the device type information is transparent to the fixed broadband network, because only IP and port information is used for identification.

## Slide 14: Issue 4: CGN related issues
Requirements:
  Long lived IPsec or TLS connection across Carrier Grade NAT (CGN) can not be flushed.
Issues:
  Currently most NAT implementations would flush all sessions after they reach 24 hours, regardless of the state of the session.
  The session flush will cause more attachment signaling to be introduced in order to re-establish UE’s sessions.

## Slide 15: Issue 5: UE mobility in FBB network
Requirements:
  The UE identification must be consistent between the FBB network and the mobile network for policy exchange, even when UE is moving.
Issues:
  Because plenty of UEs are in AP coverage at different time slot , it is possible that the same UDP port will be used for different UEs. If the UE identification can not be updated in time based on the status, the PCRF will be confused about which policy is used.
Fixed Network
PGW
Internet Service
BPCF
UE1
RG
BNG
ePDG
PCRF
SGW
MME
Mobile Network
Private IP2
Policy for UE identified by IP+Port
Public IP
(NAPT)
UE2
Private IP1
We divide the mobility capability into two cases:
UE is moving into or outside the coverage area of WiFi AP
UE’s WiFi access is dormant or not

## Slide 16: Issue 6: Flow mobility between different interfaces
Requirements:
  Traffic offloading requires the ability to move the traffic flows from one interface to the other interface of the UE.
  The type of flows to be moved depends on the policy and should be dictated by the mobile operators.
Issues:
  No flow mobility protocol has been applied for offload traffic.